## Slide 1
Control laws in the Rattlesnake
MIMO random environment
Algorithms, equations and flow charts · seven subjects · 6-12-8 system
control_laws/
15 September 2026 · sections 5–7 added after runs 09–12
Notes: This deck follows the reference document section for section. Six control laws plus the achievable-response predictor that supplies the denominator every comparison is measured against. Sections 5, 6 and 7 — pseudoinverse_control, buzz_control, and the coherence-cap behaviour — were added on 15 September after runs 09-12. The original document predated those runs and was materially incomplete: buzz in particular produced the most surprising result of the campaign.

## Slide 2
What every law receives
the control() contract
2
inputs, every cycle
specification G_xx (F,M,M)
warning / abort levels
transfer_function H (F,M,N)
noise_response_cpsd (F,M,M)
sysid_response_cpsd (F,M,M)
multiple_coherence (F,M)
frames, total_frames
extra_parameters str
last_response_cpsd G_yy (F,M,M)
last_output_cpsd X_prev (F,N,N)
output
drive CPSD X (F,N,N)
the one hard requirement
X(f) must be Hermitian positive
semidefinite at every line f.
M, N
8 control channels, 6 drives
F
901 in-band lines, 100–1000 Hz
loaded by
importlib.util.spec_from_file_location
law types
1 = generator, 2 = class, else function
X ⪰ 0 is what makes the laws differ
A drive CPSD that is not positive semidefinite is not physically realisable. How each law guarantees it — by scalar, by cone constraint, by factoring, by congruence — is the single design choice that determines both its power and its limits.
Two laws never read last_response_cpsd
pseudoinverse_control and buzz_control accept it and ignore it. They have no error term of any kind — they recompute an open-loop solve every cycle and adapt only through the FRF. Sections 5 and 6.
Notes: Every law is handed the same eleven arguments and returns one thing: the drive CPSD. The only hard requirement is that X be Hermitian positive semidefinite at every frequency line — otherwise the commanded drive is not physically realisable. Rattlesnake loads laws by file path with importlib, so there is no package context and no relative imports are possible inside a law file.

## Slide 3
Six laws, one problem, six different guarantees
3
Law | How X ⪰ 0 is guaranteed | DOF per line | Loop | rms dB, cap on
match_trace_pseudoinverse | uniform positive scalar | 1 | feedback | 8.22
optimal_diagonal_control | explicit SDP cone constraint | N² (full X) | feedback | 5.62
optimal_diagonal_control_fast | structural, X = L Lᴴ | 2Nr | feedback | 5.64
match_diagonal_congruence | structural, D X D | N | feedback | 5.31
pseudoinverse_control | automatic — congruence of G_xx | 0 (open loop) | open | 10.47
buzz_control | automatic — congruence of S′ | 0 (open loop) | open | 7.90
The guarantees buy shaping, not validity
The two open-loop laws need no machinery at all: X = H⁺ S (H⁺)ᴴ is a congruence transform of a PSD matrix, so validity is automatic. Everything the other four add buys the ability to shape the drive — and on this plant that shaping is worth between 0 and 1.1 dB against a well-chosen target.
Cap-on understates the open-loop pair
The rms column is the cap-on run for every law, which is the right setting for the four feedback laws and the wrong one for the other two. Uncapped, pseudoinverse measures 7.01 dB and buzz 5.91 — see section 7.
Notes: This is the spine of the whole document. Each law solves the same problem — choose a drive CPSD whose predicted response matches the specification — and what separates them is how they keep X positive semidefinite while doing it. Degrees of freedom per line is the useful axis: match_trace has exactly one (a scalar), congruence has N, the optimal-diagonal laws have the full matrix, and the open-loop pair has none because they do not iterate at all.

## Slide 4
match_trace_pseudoinverse
function · control_laws.py
4
The baseline, and the only law with a long validation history. One open-loop solve at startup, then a single real scalar per line.
first call — open loop
H⁺ = pinv(H, rcond)
X = H⁺ G_xx (H⁺)ᴴ
s = min(1, 10^(cap/10)·tr(G_xx)/tr(HXHᴴ))
X ← s·X
every call after — closed loop on total power
c(f) = tr(G_xx(f)) / tr(G_yy(f))
X(f) ← c(f) · X_prev(f)
Parameter string
rcond, max_drive_coherence, startup_test_level_cap_db
defaults 1e-15, 1.0, −9.0
Run | Cap | rms dB | % out | vs floor | drive V²
01 | 0.95 | 8.22 | 27.5 | 7.16 | 0.120
02 | off | 7.21 | 21.1 | 5.78 | 6.019
A pure integrator, gain 1
log X(k) = log X(k−1) + e(k−1), fed a lagged error. Simulation: ~53 cycles to settle, ~103 % peak overshoot.
Notes: Why it is safe: a uniform positive real scalar can never turn a valid drive CPSD into an invalid one, and after startup the FRF is never inverted again. Why it is limited: if channel 3 is 5 dB high and channel 5 is 5 dB low, the trace is correct and the law does nothing. Run 01 may have been saved short of convergence — its optimal single rescale is +3.37 dB, which would improve it to 7.50 dB. It is the weakest number in the comparison.

## Slide 5
optimal_diagonal_control
class · optimal_diagonal_control.py
5
Solves a semidefinite program per frequency bin for the full drive matrix, with the PSD cone as an explicit constraint.
per bin, subject to X ⪰ 0
min Σ_m ( 10·log10( [H X Hᴴ]_mm / y_m ) )²
plus an explicit coherence constraint
|X_ij| ≤ c · sqrt(X_ii · X_jj)
scheduled: only max_bins_per_update bins
are SDP-refined per call; the rest carry
the buzz baseline forward
Parameter string
rcond, ridge, max_bins_per_update, gain, max_drive_coherence
used here 1e-6, 0.05, 20, 1.0, 0.95
Run | Cap | rms dB | % out | vs floor | drive V²
03 | 0.95 | 5.62 | 11.2 | 3.99 | 0.0747
04 | off | 5.62 | 11.2 | 3.99 | 0.0790
Open defect: no startup level cap
Neither optimal-diagonal law takes startup_test_level_cap_db — it commands the full specification immediately.
Notes: Best of the set on lines-out (11.2 %) and essentially tied with congruence on rms. The cap made no measurable difference — but see the caveat: the cap reaches only SDP-refined bins, capped at 20 per call across 901 lines, so most bins carried the deliberately uncapped buzz baseline in both runs. That null result may mean "barely applied" rather than "does not matter".

## Slide 6
optimal_diagonal_control_fast
subclass · optimal_diagonal_control_fast.py
6
Same objective, but X = L Lᴴ makes positive semidefiniteness structural instead of constrained — no cone projection needed.
Burer-Monteiro factoring
X = L Lᴴ, L ∈ ℂ^(N×r)
X ⪰ 0 for ANY L — the constraint
disappears from the problem entirely
spurious-minimum threshold
r ≳ sqrt(2M) = 4 for M = 8
bm_rank was set to 6
Parameter string
rcond, ridge, max_bins_per_update, gain, max_drive_coherence, bm_rank
used here 1e-6, 0.05, 20, 1.0, 0.95, 6
Run | Cap | rms dB | % out | vs floor | drive V²
05 | 0.95 | 5.64 | 10.9 | 3.99 | 0.0760
06 | off | 5.66 | 10.7 | 3.99 | 0.0756
These runs did not test what they were meant to
The fast path disables itself when the FRF changes between calls, so runs 05 and 06 are repeats of 03 and 04.
Notes: Their close agreement with runs 03 and 04 is NOT evidence that the factored solve matches the SDP. No timing difference was observed at the rig, which is consistent with the fast path never engaging. To actually test the claim, rerun with update_tf_during_control = N.

## Slide 7
match_diagonal_congruence
class · diagonal_congruence_control.py
7
One real gain per drive per line, applied as a congruence. Keeps validity structural like the fast law, but with N degrees of freedom instead of 2Nr.
measured log error
ε_m = log(target_m / achieved_m)
sensitivity — every row sums to exactly 2
S_mi = ∂log(y_m)/∂u_i
= 2·Re(H_mi (XHᴴ)_im) / y_m
regularised Gauss-Newton, then congruence
u = argmin ‖S u − ε‖² + λ‖u‖²
D = diag(exp u); X ← D X D
Parameter string
rcond, max_drive_coherence, startup_cap_db, ridge, iters, gain, max_step_db, ceiling
used here 1e-3, 0.95, −9, 0.5, 3, 0.1, 0.5, 12
Run | Cap | rms dB | % out | vs floor | drive V²
07 | 0.95 | 5.31 | 19.8 | 3.51 | 0.0469
08 | off | 5.23 | 18.7 | 3.48 | 0.2107
Validity is structural for ANY real D
X ⪰ 0 ⟹ D X D ⪰ 0 for any real D. u_i = ε/2 for all i recovers match_trace exactly.
Notes: Best rms in the twelve-run matrix (5.23) and lowest error against the achievable floor (3.48). Also the cheapest run in the set on drive power with the cap on: 0.047 V². Its weakness is level: it sits +2.8 dB high, which costs it against the specification but not against what was reachable. That is why it leads the floor-relative ranking more clearly than the flat-spec one.

## Slide 8
pseudoinverse_control
function · control_laws.py
8
The simplest and oldest law: one open-loop solve against the raw specification, recomputed identically every cycle. No feedback, no trace management, no startup guard.
every call, identically
H⁺ = pinv(H, rcond)
X = H⁺ G_xx (H⁺)ᴴ
X ← cap(X, max_drive_coherence)
that is the entire law
last_response_cpsd is accepted
and never read
Parameter string
rcond, max_drive_coherence
defaults 1e-15, 1.0 — no third parameter
Run | Cap | rms dB | % out | vs floor | drive V²
09 | 0.95 | 10.47 | 42.1 | 9.55 | 5.449
10 | off | 7.01 | 17.8 | 5.48 | 5.377
Open defect: no startup guard at all
The only law without the first-cycle clamp. On frame one the command can be decades high.
Notes: Why it is expensive: the flat specification is diagonal and hence rank 8, while H X Hᴴ has rank at most 5 on this plant. Inverting a maximally unreachable target with no trace or coherence management burns drive power trying to manufacture response components that do not exist in the column space — 5.38 V², seventy times the optimal-diagonal family, for a worse score. Worst in the matrix on both criteria with the cap on. The cap costs it 3.47 dB; section 7 explains why.

## Slide 9
buzz_control
function · control_laws.py
9
pseudoinverse_control with one substitution — and that substitution is worth more than every feedback mechanism in the rest of this deck.
replace the spec coherence and phase
with the MEASURED ones from the buzz test
γ²_mn = |G_buzz,mn|² /(G_buzz,mm G_buzz,nn)
φ_mn = ∠G_buzz,mn
a_m = G_xx,mm # spec autospectra
S'_mn = e^(iφ_mn)·sqrt(γ²_mn · a_m · a_n)
then the same open-loop solve
X = H⁺ S' (H⁺)ᴴ
Parameter string
rcond, max_drive_coherence, startup_test_level_cap_db
defaults 1e-15, 1.0, −9.0 (shares match_trace’s parser)
Run | Cap | rms dB | % out | vs floor | drive V²
11 | 0.95 | 7.90 | 30.2 | 6.75 | 0.981
12 | off | 5.91 | 13.6 | 4.20 | 1.473
It inverts a target the plant can actually produce
The spec asks for zero coherence, which a rank-5 plant cannot give. Same solver, reachable target: 1.1 dB better.
Notes: Uncapped, buzz finishes 0.68 dB behind the best run in the entire twelve-run matrix and ahead of both match_trace runs — with no error feedback whatsoever. Second limitation worth knowing: sysid_response_cpsd is assigned only during system ID and is never refreshed during control, so the target shape is frozen for the whole run. Only the FRF adapts. The generator and class forms are NOT equivalent: neither has the cap, neither takes rcond, neither has the startup guard, and buzz_control_class.control() ignores last_response_cpsd entirely.

## Slide 10
achievable_response
not a control law · achievable_response.py
10
The denominator every comparison is measured against: for each line, the best response any physically valid drive could produce.
per line, over every valid drive
min over X ⪰ 0 of
sqrt( mean_m [10·log10(a_m / y_m)]² )
where a = diag(H X Hᴴ)
X = L Lᴴ makes X ⪰ 0 structural;
Levenberg-Marquardt, multi-restart
restrict_rcond limits L to the drive
directions surviving that cutoff
Two floors, and they agree
At rcond 1e-3 — what the laws actually invert with — the floor is 3.57–3.92 dB rms. Unrestricted but over the plant's real rank-5 subspace it is 3.56–3.90. rcond is not costing headroom; it is rejecting a direction that does not exist.
These are two independent scorings
A run's error against the floor and its error against the specification do NOT subtract. Both appear in the comparison report for that reason.
per-channel floor, dB
7X+ +0.22 8X+ +2.14 9X+ +0.39 10X+ +0.37
11X+ +0.24 12X+ +0.39 13X+ −1.79 14X+ −2.20
Notes: Not a control law — a predictor. It answers "how well could ANY law have done here", which turns a bare rms number into a meaningful one. Five channels sit inside half a dB of the specification; three carry the whole floor — 8X+ overshooting and the 13X+/14X+ pair undershooting. Those last two are the directions six shakers cannot independently command. Caution: the pooled rms (3.9) is much larger than the rms of those per-channel means (1.29) because per-line scatter is worse than the channel averages suggest.

## Slide 11
The cap inverts by family
11
Law | Loop | rms cap on | rms cap off | Δ | level on | level off
match_diagonal_congruence | feedback | 5.31 | 5.23 | −0.08 | +2.85 | +2.78
optimal_diagonal_control | feedback | 5.62 | 5.62 | −0.01 | +0.08 | +0.41
optimal_diagonal_control_fast | feedback | 5.64 | 5.66 | +0.02 | +0.26 | +0.06
match_trace_pseudoinverse | feedback | 8.22 | 7.21 | −1.01 | +0.09 | +0.05
buzz_control | open | 7.90 | 5.91 | −1.99 | +9.38 | −0.30
pseudoinverse_control | open | 10.47 | 7.01 | −3.47 | +13.55 | −1.28
1
Both open-loop solves are nearly rank one
Eigenvalue participation ratio 1.0–1.1 of 6 — the six shakers act as one source.
2
The responses cancel by precise inter-drive phasing
That phasing lives entirely in the off-diagonal terms of the drive CPSD.
3
_cap_drive_coherence shrinks exactly those terms
Diagonal preserved, so drive power barely moves — but the cancellation is destroyed and the level jumps ~20 dB.
For pseudoinverse_control and buzz_control, cap off (1.0) is the CORRECT setting
Nothing in the parameter name or the docstrings warns of it. The best achievable drive breaches 0.95 on 49 % of its pairs.
Notes: Applied to a feedback law the cap is a constraint the loop re-converges around. Applied to an open-loop law it is pure damage, because there is nothing to re-converge with. The residual is shape error, not level: the best possible single rescale of run 09's entire drive recovers only 0.30 dB. No gain correction rescues it. match_trace is the one feedback law that loses a full dB to the cap — but removing it costs 50x the drive power, so cap on is still right there.

## Slide 12
Choosing a law
Lowest error against the specification
match_diagonal_congruence, cap on or off
5.23 dB
Fewest lines outside ±6 dB
optimal_diagonal_control_fast
10.7 %
Least drive power
match_diagonal_congruence, cap on
0.047 V²
Simplest thing that works
buzz_control, cap OFF
5.91 dB, no feedback
Do not use as-is
pseudoinverse_control with the cap on
10.47 dB, +13.6 dB high
Open defects
No startup level cap on either optimal-diagonal law, or on pseudoinverse_control.
The fast law's Burer-Monteiro path never engages with FRF update on — its central claim is untested.
The optimal-diagonal coherence cap reaches only 20 of 901 bins per call.
buzz_control_generator and buzz_control_class have neither the cap nor the startup guard; the class ignores last_response_cpsd entirely.
Notes: The honest summary: on this plant, against a flat specification, the four feedback laws and the better of the two open-loop laws all land between 5.2 and 5.9 dB. That cluster is set by reachability and identification quality, not by loop design. What actually separates them is how sensibly each picks a target inside the reachable set — which is why buzz, with no feedback at all, beats match_trace, which has an integrator.